## Slide 1: Digital Interfaces and Basic PIC-C I2C Communication
Arnan (Roger) Sipitakiat
Department of Computer Engineering, Chiang Mai University, Thailand

## Slide 2: Why I2C? Case study of how an Ultrasonic Proximity Sensor works

## Slide 3: Direct Connection to the module You need to do all the timing yourself
Implement timing

## Slide 4
I2C
Take care
of timing
Offload to an I2C Host
Let an I2C host perform the timing
This idea is similar to software abstraction where you create subroutines to hide unnecessary details

## Slide 5: Tradeoffs of offloading
Benefits
  The sensor is simpler to use.
  The main processor is free to do other things.
  More modular.
Drawbacks
  More expensive
  Must be careful of timing problems on the I2C host

## Slide 6: Example 3: I2C devices on the market
Digital Clock
Barometer
Temperature & RH
Color Sensor
Accelerometer
Motor Driver

## Slide 7: Motor Driver Module
Register Address | Function
0x82 | Speed (0-255)
0x84 | PWM Frequency
0xAA | Direction (0/1)
0xA1 | Select Motor A (0/1)
0xA5 | Select Motor B (0/1)

## Slide 8: Clock Module Module address = 0xD0

## Slide 9: Bitwise Operations

## Slide 10: I2C Basics
I2C is a Bus. Serial is point-to-point
Master and Slave pair
  Master must start the communication
  Slave can only respond
Slave has a 8-bit address
  Bit 0 is reserved for direction control

## Slide 11: Basic I2C Bus Setup
MASTER
SLAVE 1
SLAVE 2
5V
Pull-up Resistors
SCL
SDA

## Slide 12: i2C Commands in PIC-C
Master Only
  I2c_start()
  I2c_stop()
Slave Only
  I2c_isr_state()
Master & Slave
  I2c_read()
  I2c_write()

## Slide 13: Sending 1 Byte to Slave
I2c_start()
I2c_write(slave addr | 0)
I2c_write(registerAddress)
I2c_write(value)
I2c_stop()
MASTER
SLAVE
Address | Content
0 | 0
1 | 0
2 | 0
3 | 0
4 | 0
5 | 0
6 | 0
7 | 0

## Slide 14: Reading 2 bytes from slave
I2c_start()
I2c_write(slave addr | 0)
I2c_write(registerAddress)
I2c_start()
I2c_write(slave addr | 1)
Value1 = I2c_read()
Value2 = I2c_read(0)
I2c_stop()
MASTER
SLAVE
Address | Content
0 | 0
1 | 0
2 | 0
3 | 0
4 | 0
5 | 0
6 | 0
7 | 0

## Slide 15: Write ค่า 50 ไปยัง Register 5 ของ slave ที่มี address = 100
I2c_start();

## Slide 16: Write ค่า 1000 ไปยัง Register 5 (ไบท์บน), 6 (ไบท์ล่าง) ของ slave ที่มี address = 100
I2c_start();

## Slide 17: Read ค่าจาก Register 5 ของ slave ที่มี address = 100
Int returnValue;
I2c_start();

## Slide 18: Read ค่าเซ็นเซอร์ 2 byte จาก Register 5,6 ของ slave ที่มี address = 100 และนำมาประกอบกันเป็นค่า int 16 Bit Register 5 = byte บน
Int16 Value;
I2c_start();

## Slide 19: Example I Controlling the Display Module Address = 0xB0
Register Address | Function
2 | High Byte
3 | Low Byte

## Slide 20: Example Program
// i2c1 - Master
#use i2c(MASTER, I2C1)
// Show the number 100 on the screen
I2c_start();
I2c_write(0xB0 | 0); // display module address
I2c_write(2); // show number command
I2c_write(0);
I2c_write(100);
I2c_stop();

## Slide 21: Example II Reading from the ultrasonic sensor